## Slide 1: Introduction to Digital Systems
Michał Kalisiak, Wiktor Porakowski Warsaw University of Technology Institute of Electronic Systems

## Slide 2: Combinational Logic
Binary adder
bin2bcd decoder
7-segment LED display driver
Truth table
Sum of Products & Product of Sums
Boolean algebra
Karnaugh map

## Slide 3
Binary adder – high level circuit
Boolean algebra

## Slide 4: The idea of the Binary Adder
Half adder
sum of 2 bits
Full adder
sum of 3 bits
8-bit adder

## Slide 5: What will we do?
Simulation Falstad circuit simulator https://www.falstad.com/circuit/circuitjs.html
3-bit adder
with 7-segment LED display
Half adder
sum of 2 bits
Full adder
sum of 3 bits
Notes: https://images-na.ssl-images-amazon.com/images/I/71ZNRbkEDAL._AC_SL1500_.jpg

## Slide 6: Truth Table + Sum of Products: AND
 | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 0
2 | 1 | 0 | 0
3 | 1 | 1 | 1
AND gate

## Slide 7: Truth Table + Sum of Products: OR
 | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 1
2 | 1 | 0 | 1
3 | 1 | 1 | 1
OR gate
using the algorithm
Minimization
Because (idempotence)
,

## Slide 8: Truth Table + Sum of Products: OR
 | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 1
2 | 1 | 0 | 1
3 | 1 | 1 | 1
OR gate
using the algorithm

## Slide 9: Boolean algebra laws
Distributivity of over
Distributivity of over
commutativity
identity
annihilation
complementation
associativity
idempotence
De Morgan’s laws
absorption

## Slide 10: Truth Table + Product of Sums: OR
 | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 1
2 | 1 | 0 | 1
3 | 1 | 1 | 1
OR gate

## Slide 11: Truth Table + Product of Sums : AND
 | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 0
2 | 1 | 0 | 0
3 | 1 | 1 | 1
AND gate
using the algorithm
minimization

## Slide 12: Logic gates
 | A | B | AND | NAND | OR | NOR | XOR | XNOR
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
2 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
3 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
 | A | B | AND | NAND | OR | NOR | XOR | XNOR
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
2 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
3 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1

## Slide 13
Binary adders
bin2bcd

## Slide 14: Half adder
We add two bits
We expect 2-bit outcome
Using Sum of Product method:
 | a | b | cout | y
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
2 | 1 | 0 | 0 | 1
3 | 1 | 1 | 1 | 0

## Slide 15: Full adder
We add three bits
We expect 2-bit outcome
Using Sum of Product method:
 | c | a | b | cout | y
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
2 | 0 | 1 | 0 | 0 | 1
3 | 0 | 1 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0 | 1
5 | 1 | 0 | 1 | 1 | 0
6 | 1 | 1 | 0 | 1 | 0
7 | 1 | 1 | 1 | 1 | 1

## Slide 16: Full adder
We add three bits
We expect 2-bit outcome
Using Sum of Product method:
 | c | a | b | cout | y
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
2 | 0 | 1 | 0 | 0 | 1
3 | 0 | 1 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0 | 1
5 | 1 | 0 | 1 | 1 | 0
6 | 1 | 1 | 0 | 1 | 0
7 | 1 | 1 | 1 | 1 | 1

## Slide 17: 4-bit bin2bcd
 | a | b | c | d | t | u3 | u2 | u1 | u0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
7 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
11 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1
12 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
13 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1

## Slide 18: 4-bit bin2bcd
 | a | b | c | d | t
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 0
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 1
11 | 1 | 0 | 1 | 1 | 1
12 | 1 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 1
15 | 1 | 1 | 1 | 1 | 1

## Slide 19: 4-bit bin2bcd
 | a | b | c | d | u3
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1
9 | 1 | 0 | 0 | 1 | 1
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0

## Slide 20: 4-bit bin2bcd
 | a | b | c | d | u2
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 1
5 | 0 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0
14 | 1 | 1 | 1 | 0 | 1
15 | 1 | 1 | 1 | 1 | 1

## Slide 21: 4-bit bin2bcd
 | a | b | c | d | u1
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0

## Slide 22: 4-bit bin2bcd
 | a | b | c | d | u0
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 1
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 1
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 1

## Slide 23: 4-bit bin2bcd
Output
Output
…

## Slide 24
Karnaugh map
bin2bcd again

## Slide 25: What have we already learned?
Theory
Truth tables
Sum of Products, PoS
Logic gates
Boolean algebra laws
Adder functions
4-bit bin2bcd
Practice
Used for buiding circuits
Minimization
Designed
Simulated

## Slide 26: 4-bit bin2bcd
 | a | b | c | d | u1
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0
reprise

## Slide 27: 4-bit bin2bcd
 | a | b | c | d | u1
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0
reprise

## Slide 28: 4-bit bin2bcd
 | a | b | c | d | u0
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 1
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 1
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 1
reprise

## Slide 29: Karnaugh map
A B | 0 | 1
0 |  | 
1 |  | 
0
1
2
3
0
0
0
1
A B | 0 | 1
0 |  | 
1 |  | 
0
1
2
3
0
1
1
1
 | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 0
2 | 1 | 0 | 0
3 | 1 | 1 | 1
 | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 1
2 | 1 | 0 | 1
3 | 1 | 1 | 1
AND
OR
Notes: https://link.springer.com/book/10.1007/978-3-319-92804-3

## Slide 30: Karnaugh map
ab cd | 00 | 01 | 11 | 10
00 |  |  |  | 
01 |  |  |  | 
11 |  |  |  | 
10 |  |  |  | 
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10
1
1
1
1
1
1
1
1
1
1
Gray code
Bits in loop
Variables in term
- no. of input bits
Notes: https://en.wikipedia.org/wiki/Gray_code

## Slide 31: 4-bit bin2bcd K-map
ab cd | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 0 | 0
11 | 1 | 1 | 1 | 1
10 | 0 | 0 | 1 | 1
 | a | b | c | d | t
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 0
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 1
11 | 1 | 0 | 1 | 1 | 1
12 | 1 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 1
15 | 1 | 1 | 1 | 1 | 1
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10

## Slide 32: 4-bit bin2bcd K-map
ab cd | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 0 | 0
11 | 0 | 0 | 0 | 0
10 | 1 | 1 | 0 | 0
 | a | b | c | d | u3
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1
9 | 1 | 0 | 0 | 1 | 1
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10

## Slide 33: 4-bit bin2bcd K-map
ab cd | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 1 | 1 | 1 | 1
11 | 0 | 0 | 1 | 1
10 | 0 | 0 | 0 | 0
 | a | b | c | d | u2
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 1
5 | 0 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0
14 | 1 | 1 | 1 | 0 | 1
15 | 1 | 1 | 1 | 1 | 1
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10

## Slide 34: 4-bit bin2bcd K-map
 | a | b | c | d | u1
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10
ab cd | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 1
01 | 0 | 0 | 1 | 1
11 | 1 | 1 | 0 | 0
10 | 0 | 0 | 0 | 0

## Slide 35: 4-bit bin2bcd K-map
ab cd | 00 | 01 | 11 | 10
00 | 0 | 1 | 1 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 1 | 1 | 0
10 | 0 | 1 | 1 | 0
 | a | b | c | d | u0
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 0
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 1
10 | 1 | 0 | 1 | 0 | 0
11 | 1 | 0 | 1 | 1 | 1
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 1
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 1
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10

## Slide 36
7-segment LED display & driver

## Slide 37: 7 segment LED display (common cathode)
cathode
anode
Notes: https://www.coilgun.info/levitation/images/led_conduction_curve.gif

## Slide 38: Driver
 | A | B | C | D | a | b | c | d | e | f | g
0 | 0 | 0 | 0 | 0 | w | e |  | h | a | v | e
1 | 0 | 0 | 0 | 1 | t | o |  | f | i | l | l
2 | 0 | 0 | 1 | 0 | i | t |  | p | r | o | p
3 | 0 | 0 | 1 | 1 | e | r | l | y |  |  | 
4 | 0 | 1 | 0 | 0 | w | e |  | h | a | v | e
5 | 0 | 1 | 0 | 1 | t | o |  | f | i | l | l
6 | 0 | 1 | 1 | 0 | i | t |  | p | r | o | p
7 | 0 | 1 | 1 | 1 | e | r | l | y |  |  | 
8 | 1 | 0 | 0 | 0 | w | e |  | h | a | v | e
9 | 1 | 0 | 0 | 1 | t | o |  | f | i | l | l
10 | 1 | 0 | 1 | 0 | - | - | - | - | - | - | -
11 | 1 | 0 | 1 | 1 | - | - | - | - | - | - | -
12 | 1 | 1 | 0 | 0 | - | - | - | - | - | - | -
13 | 1 | 1 | 0 | 1 | - | - | - | - | - | - | -
14 | 1 | 1 | 1 | 0 | - | - | - | - | - | - | -
15 | 1 | 1 | 1 | 1 | - | - | - | - | - | - | -
VALID DATA
NOT IMPORTANT
Notes: Check datasheet CD4543B

## Slide 39: 7 segment LED driver
 | A | B | C | D | a
 | 0 | 0 | 0 | 0 | 1
 | 0 | 0 | 0 | 1 | 0
 | 0 | 0 | 1 | 0 | 1
 | 0 | 0 | 1 | 1 | 1
 | 0 | 1 | 0 | 0 | 0
 | 0 | 1 | 0 | 1 | 1
 | 0 | 1 | 1 | 0 | 1
 | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 1 | 1
ABCD | 00 | 01 | 11 | 10
00 | 1 | 0 | 1 | 1
01 | 0 | 1 | 1 | 1
11 | - | - | - | -
10 | 1 | 1 | - | -
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10

## Slide 40: 7 segment LED driver
 | A | B | C | D | b
 | 0 | 0 | 0 | 0 | 1
 | 0 | 0 | 0 | 1 | 1
 | 0 | 0 | 1 | 0 | 1
 | 0 | 0 | 1 | 1 | 1
 | 0 | 1 | 0 | 0 | 1
 | 0 | 1 | 0 | 1 | 0
 | 0 | 1 | 1 | 0 | 0
 | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 1 | 1
ABCD | 00 | 01 | 11 | 10
00 | 1 | 1 | 1 | 1
01 | 1 | 0 | 1 | 0
11 | - | - | - | -
10 | 1 | 1 | - | -
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10

## Slide 41: 7 segment LED driver
 | A | B | C | D | d
 | 0 | 0 | 0 | 0 | 1
 | 0 | 0 | 0 | 1 | 0
 | 0 | 0 | 1 | 0 | 1
 | 0 | 0 | 1 | 1 | 1
 | 0 | 1 | 0 | 0 | 0
 | 0 | 1 | 0 | 1 | 1
 | 0 | 1 | 1 | 0 | 1
 | 0 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 1 | 1
ABCD | 00 | 01 | 11 | 10
00 | 1 | 0 | 1 | 1
01 | 0 | 1 | 0 | 1
11 | - | - | - | -
10 | 1 | 1 | - | -
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10

## Slide 42: 7 segment LED driver
 | A | B | C | D | g
 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 1 | 0
 | 0 | 0 | 1 | 0 | 1
 | 0 | 0 | 1 | 1 | 1
 | 0 | 1 | 0 | 0 | 1
 | 0 | 1 | 0 | 1 | 1
 | 0 | 1 | 1 | 0 | 1
 | 0 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 1 | 1
ABCD | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 1
01 | 1 | 1 | 0 | 1
11 | - | - | - | -
10 | 1 | 1 | - | -
0
1
2
3
4
5
7
6
12
13
14
15
8
9
11
10

## Slide 43
Thank you for you attention!